## Slide 1: Diagrams to Azure Networking Open Source Lab

## Slide 2: Overall design
VPN
VPN
myVnet3 (10.3.0.0/16)
myVnet2
(10.2.0.0/16)
myVnet1
(10.1.0.0/16)
myVnet4
(10.4.0.0/16)
myVnet5
(10.5.0.0/16)
VPN gateway
VPN gateway
vnet peering
vnet peering
IPSec tunnel with BGP
VM1-1
(10.1.1.4)
VM2-1
(10.2.1.4)
VM3-1
(10.3.1.4)
VM5-1
(10.5.1.4)
ubuntu-based NVAs
(10.4.2.101, .102)
vnet peering

## Slide 3: vnet internal design
vNet “MyVnetX”
IP space: 10.X.0.0/16
Subnet 2: 10.X.2.0/24
Subnet 3: 10.X.3.0/24
Subnet 1: 10.X.1.0/24
GatewaySubnet:
10.X.0.0/24
Ubuntu VM
.4

## Slide 4: lab 1: spoke-to-spoke over the VPN gateway
10.1.1.0/24
.4
10.2.1.0/24
.4
10.4.0.0/24
Ubuntu VM
Ubuntu VM
vnet gateway in mzVnet4
UDR:
10.1.1.0/24 -> vnet gw‘s internal IP
VPN
UDR:
10.2.1.0/24 -> vnet gw‘s internal IP

## Slide 5: lab 1: inter-vnet firewalling
10.1.1.0/24
.4
10.2.1.0/24
.4
10.4.2.0/24
.101
Ubuntu VM
Ubuntu VM
Firewall (iptables)
UDR:
10.2.1.0/24 -> 10.4.2.101
UDR:
10.1.1.0/24 -> 10.4.2.101

## Slide 6: lab 2: microsegmentation
10.1.1.0/24
.4
.5
10.4.2.0/24
.101
Ubuntu VM
Ubuntu VM
Firewall (iptables)
UDR:
10.1.1.0/24 -> 10.4.2.101

## Slide 7: VPN connection without NVA
.4
.4
Ubuntu VM
Ubuntu VM
VPN
VPN
10.5.1.0/24
10.4.0.0/24
10.1.1.0/24
vnet peering
IPSec VPN
Vnet
Gateway
(Vnet4)
Vnet
Gateway
(Vnet5)

## Slide 8: VPN connection with NVA
.4
.4
Ubuntu VM
Ubuntu VM
VPN
VPN
10.5.1.0/24
10.4.0.0/24
10.1.1.0/24
vnet peering
IPSec VPN
Vnet
Gateway
(Vnet4)
Vnet
Gateway
(Vnet5)
10.4.2.0/24
.101
Firewall (iptables)
UDR:
10.5.0.0/16 -> 10.4.2.101
UDR:
10.1.1.0/24 -> 10.4.2.101

## Slide 9: NVA Scale out
10.1.1.0/24
.4
.5
10.4.2.0/24
.101
Ubuntu VM
Ubuntu VM
Firewall
(iptables)
UDR:
10.1.1.0/24 -> 10.4.2.100
.102
.100
Firewall
(iptables)
Azure Load
Balancer
SNAT:
each firewall source-nats the traffic to its own address, in order to attract return traffic and thus prevent asymmetric routing

## Slide 10: NVA routing and LB probes
10.4.2.0/24
.101
.102
nva-1
nva-2
10.4.3.0/24
.101
.102
.100
lb-int
lb-ext
Traffic from VMs
Traffic from Internet
Probe
Probe
Probe
Probe
All LB probes (from both LBs) sourced from IP address 168.63.129.16
Should I send traffic back to 168.63.129.16 over eth0 or eth1?
eth1
eth0
eth1
eth0
Answer: it depends on the interface
you got the probe!
How do you do that? In Linux with custom route tables (similar to Policy-Based Routing)

## Slide 11: NVA VM Scale Set
10.4.2.0/24
Ubuntu VM
Ubuntu VM
UDR in vnet1-subnet1:
10.1.1.0/24 -> 10.4.2.100 (for intra-subnet traffic filtering)
10.2.0.0/16 -> 10.4.2.100 (for inter-vnet traffic filtering)
0.0.0.0/0 -> 10.4.2.100 (for Internet outgoing traffic filtering)
.100
VMSS with Linux-based NVAs (iptables)
Internal LB
SNAT:
each firewall source-nats the traffic to its own address, in order to attract return traffic and thus prevent asymmetric routing
DSR:
DSR rules (today port-specific) forward traffic to one of the NVAs
Single-NIC:
VM Scale Sets support only single-NIC VMs
External LB
Incoming traffic:
External LB used for incoming traffic from the internet over LB rules (today port-specific, cannot collide with ILB rules)
As a consequence, both LBs must be associated to the same NIC in the NVA. Today that can be done only using non-overlapping TCP ports.
10.1.1.0/24
.4
10.2.1.0/24
.4
UDR in vnet2-subnet1:
10.2.1.0/24 -> 10.4.2.100 (for intra-subnet traffic filtering)
10.1.0.0/16 -> 10.4.2.100 (for inter-vnet traffic filtering)
0.0.0.0/0 -> 10.4.2.100 (for Internet outgoing traffic filtering)

## Slide 12: NVA VM Scale Set: problem
10.4.2.0/24
VM1
VM2
.100
VMSS with Linux-based NVAs (iptables)
Internal LB
with DSR rule
10.1.1.0/24
.4
10.2.1.0/24
.4
X
Packets disappear somewhere between the NVA and VM1
Point | Src IP | Dst IP
1 | 10.1.1.4 | 10.2.1.4
2 | 10.1.1.4 | 10.2.1.4
3 | NVA_SRC_IP | 10.2.1.4
4 | 10.2.1.4 | NVA_SRC_IP
5 | 10.2.1.4 | 10.1.1.4
1
2
3
4
5